## Slide 1
VIS 2225 | Assignment
Yubo Zhao
Gabled Urbanism

## Slide 2
VIS 2225 | Assignment
Yubo Zhao
Design Goal
// This project is inspired by the urban fabric registered by a continuous landscape of gable roofs in historical European towns. The design will address this endless repetitive pattern of gable-ness through a code that makes the tool path “weave” around the mill board not only planarly but along the Z-axis as well to carve out the form.
// Image: https://www.britannica.com/technology/gable

## Slide 3
VIS 2225 | Assignment
Yubo Zhao
The Code | Data Structure
1
2
3
// The code is basically comprised of three major classes as components: the Coordinate class, the Grid class, and the Weaving class.
A Coordinate
(iX, iY, Point3d)
A Coordinate
(iX, iY, Point3d)
…
A Grid
(the list of Coordinates)
A Weaving
(start point)
The first Coordinate
MulWeaving
Mapping on the grid
Final Tool Path
Add some paths to make it continuous
Position
An enum class to track the positional status of every Coordinate

## Slide 4
VIS 2225 | Assignment
Yubo Zhao
The Code | Data Structure Coordinate Class
// The Coordinate class has methods like ChangePosStatus, ChangeIndex, DrawPt, and Translate.
// A Coordinate is comprised of its geometric coordinate Point 3d origin, its X/Y indices in the Grid int iX and iY, and its Positional status enum pos.
// The starting point of everything is a simple Coordinate(0, 0, Point3d()) with Position Inner.

## Slide 5
VIS 2225 | Assignment
Yubo Zhao
The Code | Data Structure Grid Class
// The Grid class has methods like ChangeRes, ChangeSize, DrawGridPts, and TranslateGrid.
// A Grid is comprised of a list of Coordinates cLst, its resolution int res, and its size double size.
// The constructor of Grid class reassigns the Position class to each Coordinate element in its cLst, for instance, the 4/9/14/19 will be assigned to OuterY, the 20/21/22/23 will be assigned to OuterX, the 24 will be Vertex, and the rest will be Inner.

## Slide 6
VIS 2225 | Assignment
Yubo Zhao
The Code | Data Structure Grid Class
// The most important method in Grid class is DrawGridLne. This method allows a continuous tool path going through the whole grid with minimal length of overlapped path.
// It basically goes as s-shape in one direction to draw the path along the Y-axis and then change its direction to draw it along the X-axis.

## Slide 7
VIS 2225 | Assignment
Yubo Zhao
The Code | Data Structure Weaving Class
// A Weaving class generates a polyline that forms a shape of X in sectional view through its DrawOne function.
// The constructor takes a start point, the degree of the inclining angle, the distance of the turn, and the length of the whole span.
// The ChangeStart method will be used to use the current “end” point as a “start” for next Weaving segment.
Section
Plan
dis
degree
length
degree
dis
length
start
end

## Slide 8
VIS 2225 | Assignment
Yubo Zhao
The Code | Data Structure Weaving Class
// The MulWeaving method is used to generate multiple Weaving segment into a polyline by using ChangeStart through a while loop.

## Slide 9
VIS 2225 | Assignment
Yubo Zhao
The Code | Tool Path Logic
Main Function
// Step 1: Input parameters(res, size, start point) to create a Grid.
// Step 2: Use the density parameter to set the dis variable for Weaving.
//Step 3: Use a while loop to draw multiple Weavings with the parameter degree on every column of the Grid, and make sure the tool path always return to the bottom to start drawing.
//Step 4: Concatenate two lists of polylines—the grid and the weaving pattern—and make sure that are one continuous path.
//Step 5: Calculate the time and the length.

## Slide 10
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 1
A steep gabled urbanism
// Configuration:
Size: 4.8; degree: 0.075 (*Pi); res: 5; density: 2

## Slide 11
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 1
A steep gabled urbanism
Plan
// Slightly adjust the grid to make sure there is not undercuts on Z-axis.
Section

## Slide 12
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 1
A steep gabled urbanism
Tool Path
Nozzle
Boolean Out
Milled Block

## Slide 13
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 1
A steep gabled urbanism
// This iteration creates a 4*4 city block with steep and pointy gables. At the street level a continuous set of building-scale facades is registered through the steep gables.

## Slide 14
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 2
A gradual gabled urbanism
// Configuration:
Size: 4.8; degree: 0.162 (*Pi); res: 3; density: 5
// Lower resolution but higher density of gables

## Slide 15
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 2
A gradual gabled urbanism
Plan
// Slightly adjust the grid to make sure there is not undercuts on Z-axis.
Section

## Slide 16
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 2
A gradual gabled urbanism
Tool Path
Nozzle
Boolean Out
Milled Block

## Slide 17
VIS 2225 | Assignment
Yubo Zhao
The Design | Iteration 2
A gradual gabled urbanism
// This iteration creates a 2*2 city block with gradual and flat gables. At the street level the gables have not become architecture yet but remains in a semi-landscape and semi-building formal gesture.